## Slide 1
HOPPER INFORMATION SERIES
APRILTAGS
AprilTags with Hopper
Use printed tag36h11 landmarks for identity, relative image position, orientation, and bounded centering.
TAG36H11
IDS 0–586
RELATIVE POSE
DECK 08 | APRILTAGS
Notes: AprilTags are designed visual landmarks. Hopper Studio uses tag36h11 and reports tag identity plus frame-relative center coordinates and 2D yaw.
[Sources]
- User-supplied high-resolution photograph: drone_photos/IMG_4476.jpeg
- https://april.eecs.umich.edu/software/apriltag.html
[/Sources]

## Slide 2
APRILTAG / 02
ORIGINS
AprilTags were built to give robots reliable visual landmarks
WRC | HOPPER STUDIO | INFORMATION SERIES
2 / 10
2011
AprilTag introduced
Edwin Olson, University of Michigan APRIL Lab; ICRA paper.
2016
AprilTag 2
A redesigned detector improved speed, detection rate, and false-positive behavior.
AprilTag 3
Faster + flexible
Small-tag detection, pose estimation, and more layouts/families.
TODAY
Robotics standard
Open implementations in research, ROS, calibration, navigation, and labs.
The original goal: print an artificial feature that a camera can identify and localize—even when natural visual features are unreliable.
Notes: AprilTag was introduced by Edwin Olson of the University of Michigan APRIL Laboratory at ICRA 2011. The system provides tag identity and six-degree-of-freedom localization from a single image. AprilTag 2 redesigned the detector; AprilTag 3 added faster detection, improved small-tag performance, flexible layouts, and pose estimation.
[Sources]
- https://april.eecs.umich.edu/papers/details.php?name=olson2011tags
- https://april.eecs.umich.edu/papers/details.php?name=wang2016iros
- https://github.com/AprilRobotics/apriltag
[/Sources]

## Slide 3
APRILTAG / 03
ROBOTICS TODAY
A printed tag can become a shared coordinate reference
WRC | HOPPER STUDIO | INFORMATION SERIES
3 / 10
LOCALIZATION
• Estimate a robot or camera pose relative to a known landmark.
NAVIGATION + DOCKING
• Center on a landing pad, charging station, doorway, or work cell.
CALIBRATION
• Relate cameras, robot frames, and measurement rigs with known geometry.
MANIPULATION
• Identify bins, tools, parts, or target objects for a robot arm.
SLAM + GROUND TRUTH
• Supply repeatable landmarks while testing perception and state estimation.
AR + HUMAN INTERFACES
• Anchor digital information to a physical place or object.
A tag is useful because its identity and geometry are designed—not discovered by chance.
Notes: AprilTags are used for augmented reality, robotics, and camera calibration. The pose capability makes them useful in localization, docking, manipulation, and repeatable experiments.
[Sources]
- https://april.eecs.umich.edu/software/apriltag.html
- https://github.com/AprilRobotics/apriltag_ros
- https://april.eecs.umich.edu/papers/details.php?name=olson2011tags
[/Sources]

## Slide 4
APRILTAG / 04
4 / 10
Notes: Tag anatomy: border, code cells, orientation, and quiet zone.
[Sources]
- https://april.eecs.umich.edu/software/apriltag.html
[/Sources]

## Slide 5
APRILTAG / 05
FAMILIES AND IDS
Family chooses the codebook; ID chooses one tag inside it
WRC | HOPPER STUDIO | INFORMATION SERIES
5 / 10
FAMILY
CODE DESIGN
WHEN IT FITS
tag16h5
Small code, fewer IDs
Legacy / compact demonstrations
tag25h9
More bits and separation
Legacy balance of size and robustness
tag36h11
36 data bits · minimum Hamming distance 11
Hopper Studio: IDs 0–586
tagStandard41h12
Modern standard layout
Upstream default for most new work
tagCircle49h12
Circular, space-efficient layout
Small circular objects
Never mix families in one detector configuration: the same ID number in another family is a different code.
Notes: In family names such as tag36h11, 36 indicates code/data bits and 11 indicates the minimum Hamming distance between valid codes. Hopper Studio deliberately uses tag36h11 and exposes IDs 0 through 586. The upstream AprilTag 3 repository recommends tagStandard41h12 for most new applications, but it is not the family implemented in Hopper Studio.
[Sources]
- https://github.com/AprilRobotics/apriltag
- Hopper Studio implementation: local_site/lib/apriltags.ts
[/Sources]

## Slide 6
APRILTAG / 06
6 / 10
Notes: Detection pipeline: grayscale, threshold, quads, sample, match, pose.
[Sources]
- https://april.eecs.umich.edu/papers/details.php?name=olson2011tags
[/Sources]

## Slide 7
APRILTAG / 07
7 / 10
Notes: Hopper Studio reports tag identity, frame-relative center coordinates, and 2D yaw.
[Sources]
- Hopper Studio implementation: local_site/lib/apriltags.ts and lib/vision.ts
[/Sources]

## Slide 8
APRILTAG / 08
8 / 10
Notes: Print tag36h11 markers cleanly and place them for the camera.
[Sources]
- Hopper Studio implementation: local_site/lib/apriltags.ts and components/HopperStudio.tsx
[/Sources]

## Slide 9
APRILTAG / 09
HOPPER STUDIO API
Centering needs tolerances, timeouts, and landing
WRC | HOPPER STUDIO | INFORMATION SERIES
9 / 10
BOUNDED APRILTAG CENTERING · PROGRAM.JS
1 await drone.takeOff();
2 try {
3 const centered = await vision.centerOnAprilTag(
4 drone,
5 7,
6 10,
7 5,
8 5,
9 3,
10 );
11
12 if (!centered) {
13 console.warn("Tag 7 was not centered.");
14 }
15 } finally {
16 await drone.land();
17 }
CENTER AND ALIGN
await vision.centerOnAprilTag( drone, id, power, centerSlack, angleSlack, lostSearches)
drone — DroneController used for corrective motion
id — 0…586 or "any"; default "any"
power — translation 0…100%; default 10
centerSlack — 1…35% of frame; default 5
angleSlack — 1…45 degrees; default 5
lostSearches — 1…20 scans; default 3
returns — Promise<boolean>; also has a 30 s timeout
does not — control altitude or land the aircraft
SCAN ALL TAGS
await vision.scanAprilTags(announceScan)
announceScan: boolean; default true · returns Promise<AprilTagDetection[]>
fields: id, bbox, corners, centerX/Y, yaw, hamming · throws on camera failure
TEST ONE ID
await vision.seesAprilTag(id)
id: 0…586 or "any"; default "any" · numeric IDs are rounded
returns Promise<boolean> after a fresh scan · throws on camera failure
Notes: The centering routine moves only horizontally and in yaw. It clamps arguments, gives up after the configured number of lost-tag searches, and has a 30-second overall timeout. It does not control altitude and does not land, so the calling mission owns the landing boundary. scanAprilTags and seesAprilTag always perform fresh scans.
[Sources]
- Hopper Studio implementation: local_site/lib/apriltags.ts
- Hopper Studio implementation: local_site/lib/vision.ts
- Hopper Studio implementation: local_site/lib/blockly.ts
- Hopper Studio flight API: local_site/lib/drone.ts.
[/Sources]

## Slide 10
APRILTAG / 10
10 / 10
Notes: Reliable tags require deliberate family, size, placement, lighting, timeout, and safety tests.
[Sources]
- https://github.com/AprilRobotics/apriltag
- Hopper Studio implementation: local_site/lib/apriltags.ts and lib/vision.ts
[/Sources]